## Slide 1: Access Strategy
Junxiao Shi, 2015-04-29

## Slide 2: Problem

## Slide 3: Definition
The access router strategy is a forwarding strategy designed for forwarding Interests from a router on the NDN Testbed to laptops directly connected to this router that can serve contents under the local site prefix.
/arizona/alice
/arizona/alice
/arizona/bob
ARIZONA
MEMPHIS
CAIDA
access router strategy

## Slide 4: Scenario: the last hop on Testbed
Several laptops connect to an access router.
  They are one hop away, with no intermediate router.
Links are lossy.
  The NDN Testbed uses UDP tunnels over public Internet. Packet losses can occur due to congestion.
FIB is mostly correct.
  Remote prefix registration allows a laptop to register a precise prefix, although this doesn't guarantee the laptop can serve all contents under that prefix.

## Slide 5: Problem: NCC strategy makes loss unrecoverable
NFD v0.2 recommends NCC strategy at the last hop from access router to laptops, but it doesn't work well.
In particular, after Interest is forwarded to a laptop, NCC strategy will never retry or retransmit to this laptop until InterestLifetime expires.
  When packet loss occurs, even if consumer retransmits the Interest, NCC suppresses the retransmission.
  Realtime applications cannot afford to wait for a regular InterestLifetime. They workaround by attempting to match InterestLifetime with RTT, causing other problems.

## Slide 6: Can we just "fix" NCC strategy?
No.
  NCC strategy is designed to exactly mimic CCNx 0.7.2 behavior.
  It's pretty complex and tightly coupled, and not easily changeable.
NCC strategy also has other problems. For example:
  RTT estimation uses incremental updates, which is inaccurate, especially if the "one level up" prefix doesn't have many children.
It should be replaced, not fixed.

## Slide 7: Design

## Slide 8: Idea
Multicast the first Interest to all nexthops.
When Data comes back, remember last working nexthop of the prefix; the granularity of this knowledge is the parent of Data Name.
Forward subsequent Interests to the last working nexthop. If it doesn't respond, multicast again.

## Slide 9: Flowchart (main)
new Interest arrival
has measurements for Interest Name?
multicast to all nexthops
send to last working nexthop
satisfied within RTO?
multicast to all nexthops except last working nexthop
wait
DONE
Y
N
satisfied
within suppression interval?
consumer retransmission
Y
N
(do nothing)
InterestLifetime timeout
Y
N
update measurements
is last working nexthop still in FIB entry, not the downstream, and not violating scope?
Y
N

## Slide 10: Flowchart (update measurements procedure)
Data arrival
Data from last working nexthop?
update per-prefix RTT estimator
copy from per-face RTT estimator
update per-face RTT estimator
DONE
Y
N
record last working nexthop
extend measurements lifetime

## Slide 11: StrategyInfo in Measurements table
Granularity: parent of Data Name
  eg. for incoming Data /A/B/v1/s0/<implicit-digest>, measurements are stored at /A/B/v1
  See reasons on next page.
Fields
  last working nexthop: which upstream satisfied the last Interest under this prefix
    "satisfy" means "first to respond": if face 1 has responded to an Interest and then face 2 also responds, "last working nexthop" is face 1.
  per-prefix RTT estimator: an RTT estimator for last working nexthop under this prefix
    TCP-like mean-deviation algorithm, but no multiplier
Lifetime: 8 seconds since any incoming Data

## Slide 12: StrategyInfo in Measurements table – granularity
Assumption: After first Data is returned, consumer will request sibling Data using exact Name. This assumption is true for:
  file retrieval: /name/v1/s0, /name/v1/s1, …
  ping: /site/ping/random0, /site/ping/random1, …
Why "parent of Data Name"?
  Going down to Data Name isn't useful: After Data /A/B/v1/s0 is returned, if there's another Interest for /A/B/v1/s0, it will be satisfied by ContentStore (in most cases) and won't be forwarded.
  We shouldn't aggregate too much: The producer returning /A/B/v1/s0 doesn't necessarily serve /A/C prefix, but almost always serves /A/B/v1 prefix.
  What about "two levels up"? Not bad for file retrieval, but isn't suitable for ping.

## Slide 13: StrategyInfo in Measurements table – granularity
Why not use Interest Name?
  Interest Name could be too coarse. The producer answering /A with /A/B/v1/s0 doesn't necessarily serve /A/C prefix.
Why not follow registered prefix (Routes)?
  Strategy doesn't have access to RIB. It can only access the longest-prefix-matched FIB entry.
  RIB/FIB prefix is too coarse.

## Slide 14: StrategyInfo in Measurements table – granularity
Why not record measurements on multiple/all levels?
  Recording at multiple/all levels incurs additional overhead, but doesn't bring much benefit:
    Lack of measurements causes multicasting. Multicasting is limited to those nexthops in FIB entry, which is expected to be less than five, and in many cases only one.

## Slide 15: Per-face RTT estimator
Assumption: Access router strategy operates on the last hop, and RTT of a particular laptop is mostly constant if processing delay of all apps on that laptop are similar.
Instead of having per-prefix-per-face RTT estimators in Measurements table (memory overhead), we keep per-prefix RTT estimator only for the last working nexthop, and have a global per-face RTT estimator.
When last working face is added or changed, the state of per-face RTT estimator is copied to per-prefix RTT estimator.

## Slide 16: Suppression interval, ie how often retransmission is forwarded
constant: 100ms
Task 1913 proposes exponential back-off, but it may not be the best solution.

## Slide 17: Conceptual Simulation
There's no code yet. Run algorithms in your mind.

## Slide 18: One precise nexthop
Scenario: FIB entry has a single nexthop laptopA.
What happens:
  All Interests go to laptopA, because strategy follows FIB.
  If laptopA doesn't respond to an Interest, retransmissions are allowed every suppression interval.

## Slide 19: Two precise nexthops
Scenario: FIB entry points to laptopA and laptopB, both can serve the entire prefix (eg. two synchronized repositories).
What happens:
  First Interest goes to both laptops.
  Whoever responds faster gets the next Interest.
  If a subsequent Interest is unanswered by "last working nexthop" (say, laptopA) after RTO, laptopB gets the Interest.
  If laptopB also doesn't respond, initial retransmission is allowed after RTO + suppression interval (since initial Interest), subsequent retransmissions are allowed every suppression interval.

## Slide 20: Two imprecise nexthops
Scenario:
  FIB entry /P points to laptopA and laptopB.
  laptopA can serve /P/A and /P/AA, laptopB can serve /P/<..> except /P/A and /P/AA.
  Data Name is at least three components, such as /P/Q/1.
What happens for Interest /P/A/<..>:
  First Interest goes to both laptops.
  laptopA responds, and becomes "last working nexthop".
  Subsequent Interests go to laptopA.
  If laptopA doesn't respond within RTO, Interest is sent to laptopB which won't respond; initial retransmission is allowed after RTO + suppression interval (since initial Interest), subsequent retransmissions are allowed every suppression interval.
What happens for Interest /P/B/<..>: similar to above

## Slide 21: All wrong nexthops
Scenario: all laptops in FIB entry don't respond
What happens:
  All Interests are sent to all laptops, because "last working nexthop" is never learned.

## Slide 22: Two imprecise nexthop with short Data Name
Scenario:
  FIB entry /P points to laptopA and laptopB.
  laptopA has Data /P/A; laptopB has Data /P/B; no other Data exists in the system.
What happens:
  Interest /P/A is sent to both laptops.
  laptopA responds, and is remembered as "last working nexthop" for /P prefix.
  Interest /P/B is sent to laptopA.
  laptopA cannot respond; after RTO it's sent to laptopB.
This scenario violates the assumption used in granularity choice.

## Slide 23: Laptop with fast and slow apps
Scenario:
  laptopA has app /P (delay=10ms) and /Q (delay=50ms)
  laptopB has app /P (delay=50ms) and /Q (delay=10ms)
What happens:
  First few Interests for two apps learn that:
    /P's last working nexthop is laptopA with 10ms RTT
    /Q's last working nexthop is laptopB with 10ms RTT
    laptopA's RTT is 10ms; laptopB's RTT is 10ms
  Apps on laptopA fail, but laptop isn't disconnected.
  Next Interest for /P is sent to laptopA but unanswered, and retried with laptopB, which answers after 50ms.
    /P's last working nexthop is laptopB with 20ms RTT
  Next Interest for /P is sent to laptopB, but RTO is inaccurate.
This scenario violates the assumption used in global per-face RTT estimator design.