## Slide 1: NLSR Design Revisited 2/12/2014

## Slide 2: Basic Functionality of NLSR
detect adjacencies, failures and recoveries
generate LSAs
  Note: for advertising an adjacency to a Broadcast link, all nodes on the link need to agree on a LAN name (may be done in Hello protocol)
synchronize LSAs (adjacencies, name prefixes, HR coordinates)
calculate FIB

## Slide 3: 1.1 Detecting adjacencies
Requirement: before advertising a link, need to ensure that the link is bidirectional
  Why? When you send an Interest over a link, Data will come back over the link. If the link doesn’t work in the reverse direction, the data will be dropped.
How to do this for different links?
  P-t-P links
  Broadcast links
Notes: Note: Information from Interest packets is untrustworthy (anyone can construct the same Interest), so even if it contains identifying information of the sending node, nodes other than the Interest sender should not use it in determining whether an adjacency is up.

## Slide 4: P-t-P Link Adjacencies
For a P-t-P link between A and B, bidirectional connectivity of the link means
  node A (or B): can send msgs to and receive msgs from B (or A) over the link
Simple protocol (this is what NLSR does now):
  For A:
    A sends a Hello Interest to B
    B sends a Hello Data to A upon receiving the Interest
    A declares the link A-B up.
    A periodically sends the Hello Interest to detect link failures
  B performs the same procedure to declare the link B-A up.

## Slide 5: One complication: multiple links between A and B
Why consider this situation? Common in operational networks
  This was seen often in operational networks, not necessarily for robustness, but more due to technology and link availability (e.g. cannot do a single high speed link, so use multiple slower link to achieve the high capacity goal)
Need to ensure that the Hello Interest/Data are sent to/received from a specific link among the multiple possibilities.
  the goal is for the forwarding plane to know which link(s) can be used for forwarding packets when multiple options exist to the neighbor
How to identify a link? Use the two ends of the link (node name is not enough), our proposal:
  node A’s name and local face id identifies A’s end of the link
  node B’s name and local face id identifies B’s end of the link

## Slide 6: Hello Protocol for P-t-P Links
Node A sends a Hello Interest periodically to each link (use /locallink name for scoping)
  Hello Interest name: /locallink/<network>/NLSR/hello/<num>, where <num> is a random number.
  The Interest is sent to a specific face, say <face1>.
  Note: nfd has to allow application to send message to a specific face.
Node B sends a Hello Data packet, signed using B’s NLSR key, after receiving the Hello Interest.
  Note: nfd has to allow application to know from which face a message is received.
  Hello Data name: /locallink/<network>/NLSR/hello/<num>/<nodeB>/<face2>
  The Interest is received from <face2> and Data packet is sent to the same face.
Once Node A receives the Data packet, it adds the link (<nodeA>/<face1>, <nodeB>/<face2>) to its LSA and advertises the new LSA containing a set of <link, cost>
  Loss and failure are detected through timeout. The specific mechanisms are described in later slides.
Node B performs the same procedure.
Every node’s path calculation module will use the links advertised in the LSAs to double check bidirectional connectivity.
  Node A’s LSA contains the link (<nodeA>/<face1>, <nodeB>/<face2>)
  Node B’s LSA contains the link (<nodeB>/<face2>, <nodeA>/<face1>)
  If the LSDB indicates that Node A advertises (<nodeA>/<face1>, <nodeB>/<face2>), then check whether Node B also advertises(<nodeB>/<face2>, <nodeA>/<face1>). If not, then ignore this link in path calculation.  this is done in IS-IS and OSPF.

## Slide 7: Example of Hello Protocol on a P-t-P link
A
B
3
4
6
5
A/3 | B/5
A/4 | B/6
B/5 | A/3
B/6 | A/4
A to B
Face 3
Interest: /ndn/nlsr/hello/<num>
Data: /ndn/nlsr/hello/<num>/<B>/5
Face 4
Interest: /ndn/nlsr/hello/<num>
Data: /ndn/nlsr/hello/<num>/<B>/6
B to A
Face 5
Interest: /ndn/nlsr/hello/<num>
Data: /ndn/nlsr/hello/<num>/<A>/3
Face 6
Interest: /ndn/nlsr/hello/<num>
Data: /ndn/nlsr/hello/<num>/<A>/4
Suppose A and B have two P-t-P links
A’s local face ids are 3 and 4 for the two links
B’s local face ids are 5 and 6 for the two links
Notes:
we assume NLSR can specify on which face a packet will be sent.
<num> is a random number unique to each node to make it easy to match the Hello reply with the Hello Interest.
Each node keeps a table of its links, each link identified by the two ends.

## Slide 8: Questions
Question 1: shall we advertise the adjacency before the two nodes’ LSDBs are sync’ed?
  Advertise before the LSDBs are sync’ed, since the forwarding plane can handle black-holes.
Question 2: If we put the node name in another name, it is difficult to determine where the node name starts and ends. What should be the general solution? Use a marker? Make the entire name as one component?
  Not a problem in the protocol yet, leave the question to later.

## Slide 9: Handling Broadcast Links
For a broadcast link, bidirectional connectivity of the link for a node means the following:
  The node can send msgs to and receive msgs from other nodes over the link.
How to detect bidirectional connectivity to the link?
  Naïve approach: every node periodically sends an Interest to the link and everyone replies to each Interest
  Problem: (1) only one Data packet to each Interest will be accepted by other nodes, even if multiple nodes reply; (2) If the Data packet contains important information (eg, for name selection), need to make sure that everyone will be heard at least once every period.
  Revised approach: everyone replies to only one received Interest each Hello interval
    how to do this? Random delay (we use this one), probability
    To use the random delay approach, we need to make sure that every reply will be heard by everyone else

## Slide 10: Random delay in Replying to Hello Interest on Broadcast Link
Assumption: only one reply for each Interest will be accepted on a broadcast link.
  If not, then all the nodes can reply to the same Hello Interest and we don’t need the suppression algorithm below.
Expected outcome: every node sends one Hello Interest and on average 1.5 Hello Data packets every Hello period.
  All nodes on the broadcast link have the same Hello time period T_h (similar to OSPF, unlike in IS-IS).
  The receivers of the Hello Interest use a random delay uniformly chosen from [0, T_d] to ensure only one node replies to the Hello.
  All nodes must have the same T_d. Otherwise, some nodes may not have a chance to reply.
  T_d is set to 2(N-2)d, where N is the number of observed nodes and d is the propagation delay on the broadcast link. The average delay for the first reply is 4(N-2)/N*d. (ref SRM paper: if T_d is C*d, then avg number of replies is 1+(N-2)/C and avg delay to first reply is 2C/N*d)

## Slide 11: Handling Broadcast Links (cont’d)
How to identify the broadcast link? Need a name unique over the entire network
  OSPF: interface address of the DR; IS-IS: router ID of the DR followed by circuit ID; NLSR: is it possible not to have DR?
  Option 1: advertise a random number for the link in Hello Data packet and select one out of n names
    How to ensure uniqueness over the entire network?
      Option 1.a: make the random number space really big (can’t guarantee uniqueness though)
      Option 1.b: concatenate the node name with the random number
  Option 2: concatenate each node name with its face id and select one out of n names (seems to be simplest)
  How to pick one name out of n names? Many questions
    Pre-emptive or not
    Simplest: the smallest (or largest one wins)
    Optional: use a configured priority as in OSPF and IS-IS
How to advertise the link?
  Each node on the link advertises the elected link name in its LSA (nodeLAN).
  Is this all we need? Maybe not (see the next slide).

## Slide 12: Challenge: can we get rid of DR (as in OSPF and IS-IS) in the Hello protocol?
DR in OSPF and IS-IS advertises the adjacency from the LAN to each node (LAN  node)
  Without DR, every node has to advertise an adjacency to every other node.
  Why is this a problem? Not so much about storage overhead, but mainly the dynamics. Whenever a node joins or leaves the LAN, everyone else has to advertise a new LSA (to add or delete this node from its adjacency list).
  Why do other routers need to know the LANnode adjacency?
    This information is used to double check bidirectional connectivity (LAN->node and node->LAN)! It’s an extra check just in case a node accidentally or maliciously advertises an adjacency that it does not have.
  If we don’t have the DR announcing the LANnode adjacency, how can other nodes (nodes not on the broadcast link but in the same network) be sure that nodeA is indeed connected to LAN when it sees the link nodeA->LAN?
    We have to rely on nodes to report LAN adjacency reliably.
    Is this an acceptable assumption?
DR also helps ensure uniqueness of the LAN name
  In OSPF/ISIS, LAN name is chosen as a result of the DR election.
  But we don’t have to have a DR to have a unique LAN name.
Note: in OSPF and IS-IS, DR serves other purposes, e.g., ensure reliable delivery of LSA (but NLSR doesn’t need a DR for this purpose since it uses sync)
Having a DR may seem convenient, but it brings its own issues: the need for election and backup

## Slide 13: Straw-man proposal for selecting link name and advertising LAN membership
Selecting link name
  If no link name has been chosen, each node proposes a link name in its Hello Data packet (either configured or randomly generated).
    To avoid collision, each node’s suggested link name is a number = hash(/nodename/linkname)
  The smallest name is selected.
  Any node can determine the winning name after observing the Hello Data packets for at least one Hello period.
  The selected link name is included in every node’s Hello Data packet.
  A new node can find the selected link name from other nodes’ Hello Data packets.
Advertising LAN membership in LSAs
  Each node advertises all other nodes attached to the same link in its LSA
  Even if a node mistakenly advertises its connectivity to the link in its own LSA, other nodes’ LSAs will not include it.
  To handle frequently flapping nodes, other nodes need to use a damping mechanism to decide whether to include this node’s name in its LSA (link membership), i.e., postpone including this node and the delay becomes longer every time the node flaps
Notes: Include router and use hashing, store the name in a permanent storage
Include all the nodes in the membership
Flip-flop nodes: RIP route flap damping and let everyone to report (damping for triggered updates)

## Slide 14: Hello Protocol on a Broadcast Link
Node A sends a Hello Interest periodically to the link with a scope of 2 (limit the propagation to the node directly connected to the link)
  Hello Interest name: /<network>/nlsr/hello/<num>
  The Interest is sent to the broadcast link, say <face1>.
Node B sends a Hello Data packet after a random delay, if no one else has sent a reply.
  Note: nfd has to allow application to overhear Data packets in order to withhold reply.
  Hello Data name: /<network>/nlsr/hello/<num>/<nodeB>/<face2>
  The Interest is received from <face2> and Data packet is sent to the same face.
  The Hello Data’s content contains information for selecting link name, the link name selected, Hello interval (see previous slide)
  After learning the link name and link membership (need to wait for one Hello period), it advertises a new version of its adjacency LSA containing the link (<nodeA>/<face1>, <broadcast-link-name>), the link cost, and other nodes on the link
How to make sure B’s Hello Data packet is heard by other nodes on the link.
  Option 1 for short-term: Other nodes issue the same Interest /<network>/nlsr/hello/<num> with scope=0 as soon as they receive the Interest. Note here the random number <num> serves another purpose: we don’t need complicated selectors
  Option 2 for long-term: nfd provides a service to applications that want to overhear data packets for a particular name prefix on the broadcast link (see Jun Xiao’s msg)

## Slide 15: Example of Hellos on Broadcast Links
Example
T1: Node A sends an Interest on the broadcast link
T2: Node B and C randomly delay their reply. B sends back the reply first, so C withholds its reply.
T3: Node B sends another Interest
T4: Node A and C randomly delay their reply. C sends back the reply first, so A withholds its reply.
A
B
C
A
B
C
Time
A
B
C
A
B
C
t1
t2
t3
t4
Solid line = Interest
Dotted lines = Data

## Slide 16: 1.2 Link Failure and Recovery Detection
What NLSR does now:
  Send a Hello Interest every T_h (60s default) and wait for the Hello Data.
  If Hello Data does not come back in time (1s default), send three consecutive Hello Interest with 1s interval.
  If still no Hello Data received, link is considered down.
  Hello Interest will continue to be sent every T_h.
  If Hello Data is received, consider the link up.

## Slide 17: 2. Generate LSAs
Three types for now
Prefix LSA: /<network>/NLSR/<router>/<pid>/LSA/Prefixes/<SeqNo>
  Question: (a) <network> before nlsr or (b) nlsr before <network>? (a)
  <pid> is the process id for this instance of NLSR.
  Content is a series of name prefixes
  All name prefixes of a router are in the same LSA.  different from the design before. Mainly for simplicity of implementation. Rely on link-level fragmentation if it’s bigger than MTU. (Status: Implemented)
Adj LSA:/<network>/NLSR/<router>/<pid>/LSA/Adjacency/<SeqNo>
  Content is a series of (link, cost)
  need to add support for broadcast links to current implementation.
Cor LSA:/<network>/NLSR/<router>/<pid>/LSA/Coordinates/<SeqNo>
  Content is hyperbolic coordinates
Question: router needs to create key and certificate for <pid> dynamically? Yes, this is doable.
Question: distribute keys in band? Yes, use ChronoSync to distribute the keys within NLSR, need to investigate the feasibility a bit more.

## Slide 18: 3. Disseminating LSAs
Requirements
  Convergence: synchronization of LSAs across the connected network under all situations
    eg. packet loss, link/node failure/recovery, network partition/recovery, new node, simultaneous routing updates, etc.
  Scaling: NLSR should be able to handle a large network (e.g. 100’s of nodes)
  Fast propagation of LSA changes
  Memory usage of NLSR: bounded for a given network size
  Number of message exchanges: light so that network is not congested by routing messages
We propose to use ChronoSync for this:
  Handles network failures
  memory does not grow unbounded like CCNSync, as it does not store the actual data
  Design and implementation are relatively mature (saves lots of time compared to developing a new sync ourselves)
A few issues need to be resolved in order to use ChronoSync
  NLSR has three types of LSAs (one instance of ChronoSync supports only one stream of data)  issue resolved and solution implemented in NLSR (see backup slides)
  More efficient operation on broadcast links (Sync messages containing the same digest value may be sent multiple times)
  Optional: Add piggybacking of actual LSA data in Sync Data messages
Question: sync in hop-by-hop mode or multicast mode?

## Slide 19: More Open Questions
Can we combine Hello and Sync?
  Sync Interests and Hello Interests have different semantics.
    Sync Interests are meant to be aggregated, while Hello Interests are not because, in order to declare a link up, the sender needs to be sure that its his/her Hello that’s being replied.
  Sync Data and Hello Data have different semantics.
    Sync Data means something has changed.
    Hello Data means I’m still up. Even if no LSA has changed, you still need to send Hello Data.
  Combining Sync with Hello may not necessarily reduce message overhead on a broadcast link (see my msg)
  The combined protocol is more complex.
Given the above, we will separate the two.

## Slide 20: 4. Calculate FIB
Need to add bidirectional reachability test in Dijkstra calculation (similar to IS-IS)
Improve the efficiency of multipath calculation (currently runs Dijkstra n times if node has n local links).
Need to improve the quality of the calculated paths (calculate disjoint paths)
  Our performance testing shows that link state sometimes performs worse than hyperbolic as its multiple paths tend to converge on a single node (e.g. Memphis node in the testbed topology). When this node is down, there’s no alternative paths.

## Slide 21: Backup Slides

## Slide 22: Design with ChronoSync
NLSR’s
Other
Logic
Sync
Logic
Handler
NLSR
ChronoSync
SLH: Sync Logic Handler
Updates
Seq No
LSA
updates
Updates
From Others
Interest
For
LSAs
Data
LSA
updates
Neighbor’s NLSR
C
hr
no
S
y
nc

## Slide 23: Process Steps
NLSR Start up
  Connect to CCND
  Register two prefixes
    Router prefix
    LSA Prefix
  Create an app socket to ChronoSync by C wrapper
    Register update callback function
    Register remove callback function

## Slide 24: Process Steps
NLSR builds adjacency LSA
  Publishes updates to ChronoSync
NLSR builds Name LSA
  Publishes updates to ChronoSync
NLSR builds Cor LSA
  Publishes updates to ChronoSync
NLSR publishes all updates with Router Name and global sequence number
NLSR waits for updates from ChronoSync

## Slide 25: Updates from ChronoSync
ChronoSync informs NLSR about updates by calling the update callback function
  Provides Names of updated data
  Provide Sequence No of updated data
Upon receive NLSR retrieve LSA updates from neighbor
  Send interest to neighbor for LSA
  Install LSA in LSDB
  Store encrypted LSA content to reply for same interest
  If Adjacency/Cor LSDB is changed trigger routing table calculation
  If prefix LSA then update FIB

## Slide 26: Global Sequence No
64 bit for total sequence No
  Rightmost 20 bits for Adj LSA [0-19th bit]
  20th-39th bit for Name LSA
  40th-59th bit for Cor LSA
  4 bit unused

## Slide 27: Sequence No Encoding
SeqNo=0
SeqNo=SeqNo | AdjLSASeq
SeqNo=SeqNo | NameLSASeq<<20
SeqNo=SeqNo | CorLSASeq<<40

## Slide 28: Sequence No Decoding
AdjLSASeq=SeqNO & FFFFF
NameLSASeq=SeqNO & (FFFFF<<20)
CorLSASeq=SeqNO & (FFFFF<<40)