## Slide 1: NFD forwarding pipelines
Junxiao Shi, 2014-01-28

## Slide 2: Overview
Forwarding consists of pipelines and strategies
Pipeline: a series of steps that operate on a packet or a PIT entry
Strategy: a decision maker on whether, when, and where to forward an Interest

## Slide 3: Pipelines
incoming Interest
Interest loop
outgoing Interest
Interest rebuff
Interest unsatisfied
incoming Data
Data unsolicited
outgoing Data

## Slide 4: Legend in diagrams
building block
pipeline
tables feature
strategy
face feature

## Slide 5
incoming Interest
incoming Data
outgoing Interest
outgoing Data
strategy API
original strategy
broadcast strategy
Interest rebuff
Interest unsatisfied
Interest loop
PIT delete
best route strategy
Data unsolicited

## Slide 6: incoming Interest pipeline
CS lookup
outgoing Data
PIT insert
cancel unsatisfy & straggler timer
app-chosen nexthops?
FIB lookup
dispatch to strategy
outgoing Interest
Y
Y
receive Interest
detect loop
Interest loop
Y
insert InRecord
foreach
nexthop

## Slide 7: forward according to app-chosen nexthops
Given incoming Interest, if its local control header contains nexthops chosen by application, forward to these nexthops
  Strategy is not used; outgoing Interest pipeline is still used

## Slide 8: dispatch incoming Interest to strategy
Given FIB entry and incoming Interest, determine which strategy should process this Interest, and trigger that strategy

## Slide 9: outgoing Interest pipeline
insert OutRecord
pick Interest
send Interest
set PIT unsatisfy timer
Interest unsatisfied
timer event

## Slide 10: pick outgoing Interest packet
Given PIT entry and nexthop, decide the guiders on the outgoing Interest
  Nonce and InterestLifetime come from an InRecord with longest remaining lifetime, however InRecord with same Face as the nexthop cannot be used
  InterestLifetime is carried from the original packet without deducting the time elapsed
  Scope is the most relaxed among all unexpired InRecords
  The last incoming Interest is picked
    This is a simple choice until we understand the effect of guiders better

## Slide 11: set PIT unsatisfy timer
Given PIT entry, set an unsatisfy timer which fires when InterestLifetime expires for all unexpired InRecords
When the unsatisfy timer fires, Interest unsatisfied pipeline is entered

## Slide 12: Interest rebuff pipeline
Process an Interest that has been decided that it has nowhere to go
set PIT straggler timer
timer event
PIT delete

## Slide 13: Interest loop pipeline
Process an Interest that has been considered looped
  This pipeline is currently empty, which means Interest packet is dropped. NACK support could be added here

## Slide 14: Interest unsatisfied pipeline
invoke PIT unsatisfied callback
PIT delete

## Slide 15: incoming Data pipeline
PIT match
receive Data
Y
CS insert
outgoing Data
invoke PIT satisfy callback
cancel unsatisfy & straggler timer
mark PIT satisfied
set PIT straggler timer
foreach
PIT entry
foreach
pending
downstream
Data unsolicited
timer event
PIT delete

## Slide 16: set PIT straggler timer
Given PIT entry, set a straggler timer which fires after a short time
  Tstraggler = MIN(InterestLifetime, MAX(RTT, TstragglerMIN))
  RTT=round trip time of this retrieval, if the Interest is satisfied
  TstragglerMIN=a constant on the order of 100ms
When the straggler timer fires, PIT entry is deleted
The purpose of retaining PIT entry for a short time is to facilitate loop detection and to collect measurement for non-fastest upstreams

## Slide 17: outgoing Data pipeline
traffic manager
send Data

## Slide 18: Pass-through traffic manager
Provide a traffic manager that does nothing and merely passes Data packet to the next step

## Slide 19: Data unsolicited pipeline
accept to cache?
Y
CS insert