## Slide 1: Duplicate Suppression on Multicast Face
Junxiao Shi 2015-02-11

## Slide 2: Problem
Two routers and a laptop is in the same multicast group or broadcast media.
The laptop sends an Interest to the multicast group, which is forwarded by both routers to the Internet.
Data comes back to both routers at almost the same time.
Both routers will return Data onto the multicast group.
The same Data is transmitted twice on the multicast group, which wastes bandwidth.

## Slide 3: ccnd: randomized delay
A multicast face has two content queues:
  CQ_NORMAL for most ContentObjects, 10ms base delay
  CQ_SLOW for unsolicited, 40ms base delay
Inserting a ContentObject to a queue schedules content_sender after a randomized delay [base_delay, 3*base_delay)
  if it's not already scheduled
Incoming ContentObject from a face cancels the same ContentObject in any queue of that face.

## Slide 4: ccnd: randomized delay
ContentObjects are sent in bursts.
  Each burst sends at most 2 ContentObjects, and stops after 6.6KB is sent.
  If queue is non-empty after a burst, next burst is scheduled immediately after.
A queue becomes the "preferred provider" after sending 12 ContentObjects in consecutive bursts.
A queue loses "preferred provider" state if any ContentObject is cancelled due to an incoming ContentObject being a duplicate.

## Slide 5: ccnd: randomized delay
If a queue is the "preferred provider",
  content_sender is rescheduled after a short delay (= 3 microseconds).
  If no ContentObject enters the queue in this duration, content_sender won't be rescheduled again, and "preferred provider" state is lost.
Otherwise,
  content_sender is rescheduled after a randomized delay within [base_delay, 3*base_delay).
  If no ContentObject enters the queue in this duration, content_sender won't be rescheduled again.