## Slide 1: Duplicate Suppression on Multicast Face
Junxiao Shi 2015-02-14

## Slide 2: Problem
Two upstreams and one downstream are in the same multicast group or broadcast media.
The downstream sends an Interest to the multicast group.
Both upstreams will return Data onto the multicast group.
The same Data is transmitted twice on the multicast group, which wastes bandwidth.

## Slide 3: ccnd: randomized delay
ContentObjects to be sent out of a multicast face is queued.
The first packet in queue is sent after a randomized delay between 10ms and 30ms. Subsequent packets are sent without delay.
After sending 12 packets without detecting duplicate ContentObjects from other ccnd on the same multicast group, no randomized delay will be applied for future packets, until the queue becomes empty.

## Slide 4: ccnd (details)
A multicast face has two content queues:
  CQ_NORMAL for most ContentObjects, 10ms base delay
  CQ_SLOW for unsolicited, 40ms base delay
Inserting a ContentObject to a queue schedules content_sender after a randomized delay [base_delay, 3*base_delay)
  if it's not already scheduled
Incoming ContentObject from a face cancels the same ContentObject in any queue of that face.

## Slide 5: ccnd (details)
ContentObjects are sent in bursts.
  Each burst sends at most 2 ContentObjects, and stops after 6.6KB is sent.
  If queue is non-empty after a burst, next burst is scheduled immediately after.
A queue becomes the "preferred provider" after sending 12 ContentObjects in consecutive bursts.
A queue loses "preferred provider" state if any ContentObject is cancelled due to an incoming ContentObject being a duplicate.

## Slide 6: ccnd (details)
If a queue is the "preferred provider",
  content_sender is rescheduled after a short delay (= 3 microseconds).
  If no ContentObject enters the queue in this duration, content_sender won't be rescheduled again, and "preferred provider" state is lost.
Otherwise,
  content_sender is rescheduled after a randomized delay within [base_delay, 3*base_delay).
  If no ContentObject enters the queue in this duration, content_sender won't be rescheduled again.

## Slide 7: Issues in ccnd algorithm
Delay range is fixed; it's not adaptive to link conditions
There's observation of packet reordering
  although there's no evidence in the algorithm

## Slide 8: Duplicate Suppression
Don't send Data if someone else has sent it
Drawback: Data is delayed.
  Some form of randomized delay is needed.
Drawback: Both upstreams still produce/fetch the Data, but this work is wasted on one upstream.

## Slide 9: Multicast/Unicast Switch
Downstream multicasts first Interest to learn who are the upstreams, and unicasts subsequent Interests to only one upstream of its choice.
Challenge: Downstream must guess the prefix under which an upstream is able to serve.
Benefit: There's no delay for most Data.
  In the absence of failures, delay happens only if the consumer makes wrong guess on the prefix and therefore unicasts Interest to the wrong upstream.
Benefit: Only one upstream producers/fetches the Data
  except for the first Interest.
Multicast/unicast switch is superior to duplication suppression alone as a solution to the problem.

## Slide 10: Is duplicate suppression still needed with multicast/unicast switch?
Duplication suppression is still useful even with multicast/unicast switch.
  It can be used on the Data in response to a multicasted Interest.
  It won't harm the effectiveness of multicast/unicast switch, because suppression happens only if both upstreams have produced/fetched the Data at almost same time. Consumer will learn only one upstream, but it's (almost) the fastest.
Duplication suppression is less important,
  because only the Data in response to a multicasted Interest would be transmitted multiple times if there's no duplication suppression.