## Slide 1: NFD Tunnel Authentication
Junxiao Shi, 2014-11-18

## Slide 2: Outline
Why is tunnel authentication necessary?
  Which faces need tunnel authentication?
At high level, how does tunnel authentication work?
What packets are used by tunnel authentication? How does client and server operate?
Are there any deployment issues?
How does NFD tunnel authentication compare to IP-based VPN solutions?

## Slide 3: Necessity

## Slide 4: Overlay Tunnel needs Authentication
You don't want to allow anyone in the world to gain connectivity through your router.

## Slide 5: Authentication is for Tunnels Only
Multicast faces do not need authentication: local area network is trusted.
Backbone overlay links (eg. between testbed routers) SHOULD have mutual tunnel authentication.

## Slide 6: High-level Design

## Slide 7: Feature Overview
Tunnel opening is explicit: tunnel authentication request and reply.
  Other packet exchanges are rejected before this sequence is done.
Authentication is mutual.
Keep-alive is done by repeating the tunnel opening sequence, shortly before previous one expires.
Tunnel closing can be explicit: tunnel closure request and reply.
Tunnel closing can also be implicit: failure to keep-alive closes the tunnel.

## Slide 8: Tunnel Opening (successful)
C-S: tunnel authentication request
  Interest signed by client's key
  contains a TunnelLifetime chosen by client
S-C: tunnel authentication reply
  Data signed by server's key
  contains a TunnelLifetime chosen by server
Tunnel is open.

## Slide 9: Tunnel Opening (server rejects)
C-S: tunnel authentication request
  Interest signed by client's key
  contains a TunnelLifetime chosen by client
Server does not trust the signature in the request, or does not want to establish the tunnel.
S-C: tunnel authentication reply
  Producer-generated NACK signed by server's key
  contains an error code; no error message to avoid leaking sensitive information

## Slide 10: Tunnel Opening (client rejects)
C-S: tunnel authentication request
  Interest signed by client's key
  contains a TunnelLifetime chosen by client
S-C: tunnel authentication reply
  Data signed by server's key
  contains a TunnelLifetime chosen by server
C-S: tunnel closure request

## Slide 11: Tunnel Lifetime
Tunnel lifetime is requested by client and granted by server.
  Tunnel lifetime MUST NOT be less than 2000ms, to ensure correct protocol operations.
  Server MAY grant a TunnelLifetime that is less than client's request.
Client perceives the tunnel to be open for negotiated lifetime since the moment it sends tunnel authentication request.
Server perceives the tunnel to be open for negotiated lifetime since the moment it sends tunnel authentication reply.

## Slide 12: Keep-Alive and Implicit Closing
At some random point between 50% and 75% of tunnel lifetime, client repeats tunnel opening sequence.
If a valid tunnel authentication request does not arrive at the end of tunnel lifetime as perceived by the server, the tunnel is implicitly closed.
If a valid tunnel authentication reply does not arrive at the end of tunnel lifetime as perceived by the client, the tunnel is implicitly closed.

## Slide 13: Explicit Closing
C-S: tunnel closure request
  Interest signed by client's key
  seize to send other packets; accept incoming packets
S-C: tunnel closure reply
  Data signed by server's key
Tunnel is closed.
This sequence works on the other direction as well.
Each party SHOULD first send other pending packets, wait for a short duration for them to be delivered, then send the tunnel closure request/reply.

## Slide 14: Protocol Details

## Slide 15: Deployment Issues

## Slide 16: Comparison to VPN