## Slide 1: NFD tables conceptual structure and algorithms
Junxiao Shi, 2014-01-17

## Slide 2: About
This document describes the conceptual structure of core tables in NFD, and the semantics of table algorithms
  The physical layout (eg. hashtable, tree, trie) is chosen by implementer, as long as all described algorithms can be provided
This document focuses on how table entries are organized and accessed; it does not describe every field in an entry
  Fields that need to be understood by tables are described
  Fields inside an entry are not described, such as measurement, PIT downstream/upstream records, attributes and timers
This slide deck contains animations. Enter slideshow to see them

## Slide 3: CS

## Slide 4: CS entry
CS entry contains information about a Data packet
No duplicate CS entry is allowed
  Two Data packets are duplicate if they are identical byte-by-byte
CS entry
  has a Data packet
  has the implicit digest, or indicates that the implicit digest is not yet computed
  has a stale time
  indicates whether the Data packet is unsolicited

## Slide 5: CS initialize
CS is initialized as empty

## Slide 6: CS insert
Given a Data packet, if CS admission policy permits it to be cached,
  if the Data packet is not a duplicate to any existing CS entry, create a new CS entry
  if the current Data packet is unsolicited, but the existing CS entry is not unsolicited, abort these steps
  if the current Data packet is unsolicited, mark the CS entry as unsolicited; otherwise, mark the CS entry as not unsolicited
  the stale time of CS entry is updated to now()+FreshnessPeriod
Notes for physical structure
  For supporting CS lookup algorithm, CS should be organized as an ordered sequence, sorted by canonical ordering of the Name with implicit digest
  Computation of implicit digest can be deferred until it's necessary to determine the order

## Slide 7: CS insert – deferred implicit digest computation
Name | implicit digest
/example/B | not computed
/example/C | not computed
/example/D | not computed
/example/C | not computed
…0002
…0001

## Slide 8: CS insert – deferred implicit digest computation
Name | implicit digest
/example/B | not computed
/example/C/…0001 | not computed
/example/D | not computed
/example/C | not computed
…0002

## Slide 9: CS cleanup
Periodically check the size of CS (number of CS entries). If the size is exceeding a certain threshold, evict some entries to bring the size down to the threshold
Which entries to evict is determined by CS eviction policy, such as
  unsolicited entries are evicted first
  stale entries (stale time in the past) are evicted next
  other entries are evicted by the order they are created

## Slide 10: CS lookup
Given an Interest, find the best CS entry that satisfies this Interest, or determine that no CS entry could satisfy this Interest
  in the ordered sequence, locate the starting point
    if Interest has Exclude selector that start with <Any><Compoent>K</Component> (so that anything less than or equal to K is excluded, starting point is Interest Name plus K
    otherwise, starting point is the first CS entry whose Name is greater than or equal to Interest Name
  set nameLength to the number of components in the Interest, set lastMatch to nil

## Slide 11: CS lookup
  if last component in Interest Name may be an implicit digest, compute the digest of current CS entry
    last component in Interest Name may be an implicit digest, if MinSuffixComponents is less than or equal to 1, and last component has 32 octets
  if Interest Name is not a prefix of current CS entry's Name plus implicit digest if computed, goto step 9
  if current CS entry violates MinSuffixComponents, MaxSuffixComponents, PublisherPublicKeyLocator, Exclude, MustBeFresh selectors, go to step 8
  if ChildSelector prefers leftmost child, return current CS entry
  if ChildSelector prefers rightmost child, and ((lastMatch is nil) or (current CS entry and lastMatch have different nameLength-th component)), set lastMatch to current CS entry
  move to next CS entry in the ordered sequence, and goto step 3
  return lastMatch

## Slide 12: CS lookup
Interest
Name: /example/C
ChildSelector: leftmost
Name | implicit digest
/example/B | not computed
/example/D | not computed
out of prefix

## Slide 13: CS lookup
Interest
Name: /example/C
Exclude: (-∞,m],[s,w]
ChildSelector: leftmost
MinSuffixComponents: 3
Name | implicit digest
/example/B | not computed
/example/C | not computed
/example/C/h/1 | not computed
/example/C/m | not computed
/example/C/n | not computed
/example/C/s/2 | not computed
/example/C/y/3 | not computed
/example/C/y/4 | not computed
violates Exclude
violates MinSuffixComponents
violates Exclude
matches

## Slide 14: CS lookup
Interest
Name: /example/C
ChildSelector: rightmost
Name | implicit digest
/example/B | not computed
/example/C/p/1 | not computed
/example/C/p/2 | not computed
/example/C/q/1 | not computed
/example/C/q/2 | not computed
/example/C/r/1 | not computed
/example/C/r/2 | not computed
/example/D | not computed
last match
out of prefix
nil
violates ChildSelector
violates ChildSelector

## Slide 15: CS lookup
Interest
Name: /example/C/…0002
ChildSelector: leftmost
Name | implicit digest
/example/B | not computed
/example/C | not computed
/example/D | not computed
matches
…0002