## Slide 1: Interest NACK
Junxiao Shi, 2014-07-27

## Slide 2: Introduction
Interest NACK, aka "negative acknowledgement", is sent from upstream to downstream to inform that Data could not be retrieved in response to an Interest.
Interest NACK is useful in forwarding strategy as a explicit signal, for congestion control and other purposes.
This document is a proposal for including Interest NACK in NDN-TLV packet format, and in NFD forwarding pipelines.

## Slide 3: Interest NACK vs Application NACK
Interest NACK
generated by network router
signals unavailable of Data on a certain router / path
(topic of this proposal)
Application NACK
generated by producer app
indicates non-existence of Data
is a Data packet signed by producer
(not in this proposal)

## Slide 4: Semantics

## Slide 5: Interest NACK
An Interest NACK is a packet sent by upstream to inform the downstream that Data cannot be retrieved or delivered in response to an Interest.
An Interest NACK contains an Interest and a reason code.

## Slide 6: Interest in Interest NACK
The Interest in an Interest NACK is the Interest that triggers the Interest NACK.
After an Interest packet is forwarded from downstream to upstream, the upstream can either return a Data, or return an Interest NACK that contains this Interest.
  On each point to point link, with absence of packet loss, there is a flow balance between Interests vs Data + Interest NACKs.

## Slide 7: Reason in Interest NACK
The reason code in an Interest NACK indicates why the upstream wants to send an Interest NACK in response to the enclosed Interest.
Commonly used reason codes include Duplicate, Congestion, NoData, Busy, etc (defined in this section)

## Slide 8: Reason: Duplicate
An Interest NACK with reason code Duplicate informs the downstream that the Interest is a duplicate, because the combination of Name and Nonce is previously seen by the upstream.
This means either the Interest is looped, or the Interest has reached the upstream via another path.

## Slide 9: Reason: Congestion
An Interest NACK with reason code Congestion informs the downstream that there is a congestion on the forwarding path of the Interest.
The congestion can occur on the link between downstream and upstream, or on the path from upstream toward the content source(s).
The congestion can occur in either direction.

## Slide 10: Reason: NoData
An Interest NACK with reason code NoData informs the downstream that the upstream has no route to forward the Interest.

## Slide 11: Reason: Busy
An Interest NACK with reason code Busy informs the downstream that the Interest has reached a producer, but the producer is too busy to handle this Interest.

## Slide 12: Possible extensions for Congestion and Busy
Congestion and Busy reasons both request the downstream to send less Interests. The percentage of Interest rate to be decreased should be made explicit as an additional field in the Interest NACK packet.
Multiple Interests should be aggregated in a single Interest NACK packet.

## Slide 13: Interest NACK in a multi-access group
Currently it's unclear who Interest NACK could operate in a network layer multi-access group. This proposal does not allow Interest NACKs to be transmitted on a multi-access face.

## Slide 14: Packet Format

## Slide 15: Option 1: new TLV0
InterestNack ::= INTEREST-NACK-TYPE TLV-LENGTH
Interest
NackCode
NackCode ::= NACK-CODE-TYPE TLV-LENGTH
nonNegativeInteger

## Slide 16: Option 1: new TLV0
Advantage
Processing path of Interest NACK is different from Interest or Data processing path. Having a different top-level type allows simpler classifier.
A unique type ensures Interest NACKs won't confuse routers and apps that don't understand them.
Drawback
A new packet type is defined.

## Slide 17: Option 2: Interest with extra field
Interest ::= INTEREST-TYPE TLV-LENGTH
Name
Selectors?
Nonce
Scope?
InterestLifetime?
NackCode?
When NackCode is present, it's an Interest NACK packet. When NackCode is omitted, it's an Interest packet.

## Slide 18: Option 2: Interest with extra field
Advantage
On some platforms, it's probably more efficient to convert between Interest and Interest NACK.
Drawback
A router or app that doesn't understand Interest NACK may confuse this as an Interest, and return Data to the sender of this NACK

## Slide 19: Option 3: Data with new ContentType
Interest NACK is represented as a Data.
  ContentType=NACK
  Name=/<Interest/Name>/NACK/<Selectors>/<NackCode>
Alternatively,
  ContentType=NACK
  Name=/<Interest/Name>
  payload=Selectors? NackCode
Note: ContentType=NACK means Interest NACK here; in CCNx, it means Application NACK.

## Slide 20: Option 3: Data with new ContentType
Advantage
If Data satisfies Interest,
  Flow balance between Interest and Data is maintained.
  Routers who don't understand Interest NACK can still forward them.
Drawback
This Data doesn't always satisfy Interest, due to Min/MaxSuffixComponents selectors
Data may unexpectedly satisfy other Interests (with shorter Name)
Apps who don't understand Interest NACK are confused

## Slide 21: The Choice
Option 3 is eliminated first, because the Data cannot always satisfy Interest, thus its benefits cannot be achieved.
Option 1 is preferred over option 2, because it allows easier packet classification of Interest NACK, which needs a processing path that is different from Interest or Data; it also won't confuse a router or app that does not understand Interest NACK.

## Slide 22: Should Interest NACK be signed?
A signed Interest NACK assures downstream that the NACK comes from the authentic upstream, given that the public key is pre-shared.
Signing has significant computation cost that is unaffordable in forwarding plane.
If Interest NACK is unsigned, what could malicious nodes gain?

## Slide 23: Gain of malicious node on bogus NACK
Interest NACK is a hop-by-hop message that says "I cannot retrieve this Data".
On a point-to-point link, a malicious node gains nothing for sending bogus Interest NACK.
  If a malicious node sends a bogus Interest NACK, other nodes will send less Interests toward it.
  Suppose Interest NACK must be signed, the malicious node can achieve the same effect by not sending anything.
  Generally, the situation is unfavorable to the malicious node, because it stops the traffic flow into the malicious node.

## Slide 24: Gain of malicious node on bogus NACK
On a (link layer) multi-access media, a malicious node can waste network resource and cause congestions by sending bogus Interest NACK.
  A malicious node could send a bogus Interest NACK on behalf of current upstream; address spoofing is needed to appear as a legitimate upstream.
  This won't prevent the legitimate upstream from returning Data. That returned Data would also be accepted by the downstream.
  However, this bogus Interest NACK triggers the downstream to explore alternate paths, which increases network usage on alternate paths, and possibly cause congestion on those alternate paths.
  This problem can be fixed by standard techniques of preventing Ethernet/IP address spoofing, eg. port-MAC-IP binding.

## Slide 25: Interest NACK is unsigned
Signing has significant computation cost.
A malicious node gains nothing by sending bogus Interest NACK on a point-to-point link.
A malicious node can cause congestion by sending bogus Interest NACK on a link layer multi-access media, but this attack must be used together with address spoofing. Standard techniques against address spoofing can prevent this attack.
Therefore, signing is unnecessary for Interest NACK.

## Slide 26: Forwarding Pipelines

## Slide 27: Incoming NACK pipeline
PIT match
receive NACK
trigger strategy: after receive NACK
(drop)
mark out-record as NACKed
N
has out-record?
Y
(drop)
N
Y

## Slide 28: Outgoing NACK pipeline
send NACK
strategy action: send NACK
mark in-record as NACKed
has in-record?
(drop)
N
Y

## Slide 29: NACKed field in PIT in-record
A NACKed field is added to PIT in-record.
This field is cleared in Incoming Interest pipeline.
This field is set to the reason code in Outgoing NACK pipeline.
The purpose of this field is to help forwarding strategy make decisions.

## Slide 30: NACKed field in PIT out-record
A NACKed field is added to PIT out-record.
This field is cleared in Outgoing Interest pipeline.
This field is set to the reason code in Incoming NACK pipeline.
The purpose of this field is to help forwarding strategy make decisions.