## Slide 1: Link Service
Junxiao Shi, 2015-08-14

## Slide 2: Outline
Introduction
Design of generic link service

## Slide 3: Introduction

## Slide 4: What is Link Service
Link Service is a part in NFD Face System providing face features universal to all socket types, such as:
  NDNLP
  face authentication
  network-layer counters

## Slide 5: Face architecture with LAL
Face
Forwarding
Socket
generic link service
vehicular link service
UNIX link
Ethernet link
UDP link
TCP link
network layer packet: Interest, Data, Nack
TLV Block
UNIX/TCP stream, Ethernet frame, UDP packet

## Slide 6: LinkService needs to be modular
Network environment dictates what features are needed in LinkService.
  LinkService designed for routers, workstations, and mobile phones is unlikely to work well in vehicular networks or sensor networks.
  Even if all environments can agree on using NDNLPv2 as the universal packet format, different NDNLPv2 features (defined or to-be-defined) would be enabled.

## Slide 7: LinkService needs to be modular
Generic LinkService
fragmentation
failure detection
reliability improvement
…
Vehicular LinkService
over-earing implicit-ack
retransmission
cite: G. Pau 2013-08-11 AsiaFI

## Slide 8: LinkService needs to be modular
A single LinkService that covers all possible NDNLPv2 features would be extremely complicated.
  NDNLPv2 is designed to operate as a single layer. Interaction between features must be carefully planned, to allow them work together.
    eg. BFD feature transmits an IDLE packet only if no packet has been transmitted by other features in Tidle.
  It's much easier to design a LinkService for a selected subset of NDNLPv2 features, because there are less interactions to consider.

## Slide 9: Generic LinkService

## Slide 10: GenericLinkService
The GenericLinkService is a link service design that covers these NDNLPv2 features:
  indexed fragmentation
  ARQ
  BFD
  HMAC
  NACK
  extra fields for forwarding: NextHopFaceId, HopLimit, CachePolicy, IncomingFaceId
Every feature can be individually turned on or off.

## Slide 11: Send Path
encode net packet
Interest/Data/Nack
+ Tags for:
HopLimit
IncomingFaceId
Block of network layer packet
+ LpPacket header (for first fragment) with:
HopLimit
IncomingFaceId
Nack
fragmentation
assign Sequence
HMAC
LpPackets without Sequence
piggyback
ARQ
Repeat reQuest
socket
BFD
IDLE
IDLE
cache
signed LpPacket
suppress IDLE
cached LpPacket retransmission

## Slide 12: Receive Path
HMAC
reassembly
BFD
socket
ARQ
keep alive
detect gap; Repeat reQuest
verified LpPacket
decode net packet
Block of network layer packet
+ LpPacket of first fragment, contains:
Nack
NextHopFaceId
HopLimit
CachePolicy
Interest/Data/Nack
+ Tags for:
NextHopFaceId
HopLimit
CachePolicy

## Slide 13: Intermediate Packet Structure
struct Packet {
union {
shared_ptr<Interest> interest;
shared_ptr<Data> data;
shared_ptr<Nack> nack;
}
shared_ptr<Block> netPacketWire;
size_t fragStartOffset;
shared_ptr<LpPacket> lpPacket;
NetworkAddress localAddr;
NetworkAddress remoteAddr;
}
// note: This is a conceptual representation, not a real C++ struct.

## Slide 14: Intermediate Packet Structure
In the send path:
  The original network layer packet is referenced for LP features to inspect.
  Forwarding can control localAddr and remoteAddr (if face represents L2 interface, and socket is capable of setting localAddr and remoteAddr).
In the receive path:
  After reassembly, the LpPacket for the first segment is reference for LP features to inspect.
  localAddr and remoteAddr are passed from socket layer to forwarding for informational purpose.