## Slide 1: NFD Permanent Face
Junxiao Shi, 2015-06-10

## Slide 2: Outline
what is a permanent face
necessity and benefit of having permanent faces
guarantees provided by a permanent face
semantics of up/down state of a permanent face
how forwarding pipelines and strategy could make use of up/down state of a permanent face
impact on RIB daemon, NLSR, and network operations

## Slide 3: Background

## Slide 4: Socket error in a face
Most NFD face types are implemented with socket API.
A socket error occurs when the underlying communication channel is broken, for example:
  a connected local application closes its client face,
  local IP address changes,
  remote NFD has crashed.
Currently, a socket error in a point-to-point face is treated as a face failure and causes NFD to close the face.
  Note: This applies to point-to-point faces only. A socket error in a multi-access face would not cause NFD to close the face.

## Slide 5: "Persistent" face: still affected by socket error
A face has a persistency property:
  A face has persistency=on-demand if it's created by accepting an incoming connection.
  A face has persistency=persistent if it's created by a management command.
An on-demand face is closed automatically if it's left idle for a certain duration. A persistent face does not have such idle timeout.
However, both on-demand and "persistent" faces cannot survive a socket error. When socket error occurs, the face is closed.

## Slide 6: Consequence of closing a face
When a face failure occurs, NFD closes the face, which triggers a chain of events:
  FIB nexthop records referencing the failing face are removed.
  A "face destroy" notification is sent.
  Upon notification, RIB routes referencing the failing face are removed.
  If an external process sends a management command to create a face toward the same peer, the new face would have a different FaceId.

## Slide 7: Is this desirable?
Is it desirable that a face is closed when there's a socket error?
Sometimes, it's desirable:
  An end host moves to a new network; the tunnel to the old network's gateway router should be closed.
Sometimes, it's undesirable:
  see next two examples

## Slide 8: Backbone tunnel
In a large NDN network where UDP tunnels are used as backbone links, those tunnels should not be closed upon socket errors.
In today's NDN testbed, backbone tunnels are created by NLSR, because NFD is unable to make backbone tunnels permanent. But,
  Maintaining tunnels shouldn't be the responsibility of a routing daemon.
  This doesn't work well because NLSR cannot quickly detect when the temporary link error has resolved.

## Slide 9: Unattended device
In a home network where an unattended device (eg. a temperature sensor) connects to the home router over a UDP tunnel, the tunnel should be kept even if the home router reboots.
When the home router reboots, the device may see a socket error and its NFD would close the face, causing the device to lose connectivity.
Although the device could be scripted to reconnect periodically or upon face destroy notification, it's desirable not to disconnect in the first place.

## Slide 10: Introduction

## Slide 11: What is permanent face?
A permanent face is a face maintained by NFD, not affected by failures, and kept until destroyed by management.
A face can be marked as a permanent face by setting its persistency property to a new value "permanent".

## Slide 12: UP/DOWN state
A face has a "link state" property:
  UP: the face is available to transmit and receive packets
  DOWN: the face cannot transmit and receive packets
Transition between UP and DOWN link states should trigger face status change notifications.
Forwarding should notice when a face is DOWN:
  avoid sending Interests on this face,
  not expect Data coming back on this face.

## Slide 13: Socket error on permanent face
A socket error is still a face failure.
When a face failure occurs on a permanent face, instead of closing the face, NFD would:
  set the face to DOWN state
  recreate or reconnect the socket, retry indefinitely, until connectivity is reestablished
  set the face to UP state
During this process:
  FaceId remains unchanged.
  FIB nexthop records and RIB routes are not removed.
  The face may be destroyed with a management command.

## Slide 14: Face Implementation

## Slide 15: Face Types
Permanent face SHOULD be implemented for:
  UDP unicast: used by majority of backbone links
Permanent face MAY be implemented for:
  TCP: used by some backbone links; implementation is more difficult because it involves reconnecting
Permanent face is not applicable to:
  UNIX socket, TCP local, WebSocket: NFD does not make outgoing connection for those face types, so all faces are on-demand
  UDP multicast, Ethernet multicast: not point-to-point

## Slide 16: BFD and permanent face
NDNLPv2 BFD feature should be used on a permanent face.
When a face is DOWN, BFD feature can detect when the face can go UP again.
When a face is UP, BFD feature can detect a failure and declare the face as DOWN.
  Socket errors can be handled by BFD feature as a signal of face failure.

## Slide 17: Forwarding Changes

## Slide 18: Don't send Interest to DOWN face
Strategy SHOULD notice an upstream face is DOWN, and SHOULD NOT send Interests to this face.
If a strategy attempts to send an Interest to a DOWN face, a PIT out record will be created, but the face SHOULD NOT transmit the Interest.

## Slide 19: Don't expect Data from DOWN face
Strategy MAY be triggered when an upstream face to which an Interest has been forwarded goes DOWN. When triggered, strategy MAY either try alternate paths, or return NACK to downstreams.
The trigger is per PIT entry, because strategy is unable to enumerate the PIT.
  But this implies forwarding needs to enumerate PIT when a face goes DOWN. This carries a significant overhead. Optimization, such as "per-face pending Interest list", is needed.

## Slide 20: Don't return Data to DOWN face
Forwarding MUST notice a downstream face is DOWN, and MUST NOT return Data/Nack to this face.
Strategy MAY be triggered when all downstreams of a PIT entry go DOWN. When triggered, strategy SHOULD stop trying more alternate paths for this PIT entry.

## Slide 21: Impacts

## Slide 22: Impact on RIB
No semantic or functionality change is needed for RIB.
RIB updates would be less frequent because there are less face destroy events.

## Slide 23: Impact on end host operation
An end host user won't worry anymore about losing connection due to underlying connection errors.
  When a permanent face creation command line is written into NFD startup script, the user can rest assumed that the connection would be available whenever underlying network permits.
Prefix registration won't be lost due to face failures.
  When a permanent face reconnects, existing routes are kept.

## Slide 24: Impact on NLSR
Faces for backbone link SHOULD NOT be created by NLSR. Instead,
NFD startup script creates backbone link faces.
  Neighbor router name and routing cost are set as part of "face description".
NLSR, upon initialization, requests a face dataset with query condition Persistency=permanent, and connects to adjacent routers.
NLSR monitors face status change events, and updates its Adjacency LSA when face goes UP/DOWN.

## Slide 25: Impact on network operations
Backbone links are defined in NFD startup script, not in NLSR configuration file.
It's possible to add or remove backbone links without restarting NLSR.