## Slide 1: NDNLPv2
Junxiao Shi, 2015-04-28

## Slide 2: Outline
This document recalls the history of NDN link protocols, presents the format of NDNLPv2, describes its semantics, and discusses design choices.
TLDR: if you don't have time to review the whole document, please look at "Goals" section, "Packet Format" section, and "Introduction" pages in other sections.

## Slide 3: History

## Slide 4: NDNLPv1 features
NDNLPv1 was designed in 2012 as a link protocol for NDN. It solves two major issues to enable NDN directly on Ethernet:
  messages larger than Ethernet MTU cannot be sent
  packet losses may degrade application performance
NDNLPv1 provides two features:
  fragmentation and reassembly
  acknowledgement and retransmission

## Slide 5: NDNLPv1: packet types
NdnlpData contains a fragment of an Interest or a ContentObject (aka Data). Its header has:
  sequence number
  fragment index and fragment count
  a flag to request link acknowledgement
NdnlpAck contains acknowledgements for one or more fragments
  Acknowledgements are organized into blocks, where each block has a bitmap to indicate the receipt status of fragments in a consecutive range of sequence numbers. (similar to TCP SACK)

## Slide 6: NDNLPv1: fragmentation operations
The sender chops a message into fragments, and send them using consecutive sequence numbers.
The receiver reassemble fragments into messages.
  Each message has a "message identifier" that can be calculated from any fragment by subtracting fragment index from sequence number.

## Slide 7: NDNLPv1: link acknowledgement operations
The sender retains recently sent fragments.
The receiver stashes sequence numbers of received fragments, and sends all acknowledgements once per 2x link delay.
The sender expects every fragment to be acknowledged within 4x link delay. It retransmits unacknowledged fragments, at most twice per fragment within 32x link delay, and gives up after that.

## Slide 8: NDNLPv1 Multicast Extension
NDNLPv1 was initially designed for unicast link only.
Multicast extension was added in 2013.
Fragmentation operations:
  The sender operates in the same manner.
  The receiver needs to distinguish sender address. Fragments of different (sender address, destination address) are processed separately.
Link acknowledgement is no longer supported, because packet loss is believed to be uncommon on wired Ethernet.

## Slide 9: NDNLPv1-TLV
In 2014, NDN-TLV packet format is adopted. NDNLPv1 is also changed from CCNB format to TLV format.
Semantics are unchanged.
Fragmentation feature is implemented in NFD v0.1.

## Slide 10: NDNLP-BFD: failure detection
NDNLP-BFD provides failure detection on a point-to-point link.
Each host transmits at least one packet periodically (~100ms).
  This could be regular packets, or a keep-alive packet when there's no other packets to transmit.
  The peer should respond ack packets to keep-alives.
The peer is assumed failed if not heard from within a fail period (~300ms).

## Slide 11: NFD LocalControlHeader
NFD has a LocalControlHeader to carry information between forwarding daemon and privileged application on the same host.
Those information include:
  NFD tells apps where a packet come from.
  Apps tell NFD where to forward an Interest.
  Apps tell NFD about constraints on local caching.
  NFD delivers packets matching a filter to a monitoring app. (planned feature; not what ndndump uses today)

## Slide 12: Goals

## Slide 13: Features
fragmentation and reassembly
  fragment a network-layer packet to fit in link MTU
reliability
  reduce packet loss
failure detection
  rapidly detect link failure and recovery
integrity
  prevent packet injection
forwarding instruction
  NACK, nexthop choice, cache control, etc
packet information
  for management and monitoring

## Slide 14: Unified Header
The same NDNLPv2 header can be used on all kinds of links.
  Different endpoints:
    point-to-point between app and forwarder
    point-to-point between two forwarders
    multi-access among a semi-fixed group
      eg. non-NDN Ethernet switch; Ethernet repeater
    broadcast among a highly dynamic group
      eg. vehicular network (in ad-hoc environment)
  Different transports:
    datagram transport
    stream transport

## Slide 15: Modular Features
Different links need different features, or different designs of a feature.
  eg. fragmentation is unnecessary with stream transport; reliability needs to be designed differently on a point-to-point link vs on a highly dynamic multi-access group.
Therefore, NDNLPv2 needs to ensure:
  All features are optional. When a feature is unused, its fields shouldn't appear in the header.
  Different designs of a feature can be adopted.

## Slide 16: Packet Format

## Slide 17: NdnlpPacket
NdnlpPacket ::= NDNLP-PACKET-TYPE TLV-LENGTH NdnlpHeader NdnlpFragment? NdnlpTrailer?

## Slide 18: NdnlpHeader
NdnlpHeader ::= NDNLP-HEADER-TYPE TLV-LENGTH NdnlpSequence? .. NdnlpNop?
NdnlpSequence ::= NDNLP-SEQUENCE-TYPE TLV-LENGTH fixed-width unsigned integer
NdnlpNop ::= one or more zeros

## Slide 19: NdnlpFragment
NdnlpFragment ::= NDNLP-FRAGMENT-TYPE TLV-LENGTH byte+

## Slide 20: NdnlpTrailer
NdnlpTrailer ::= NDNLP-TRAILER-TYPE TLV-LENGTH .. NdnlpNop?

## Slide 21: Outermost Packet
Hosts communicating on a NDNLPv2 link MUST allow both NdnlpPackets and bare network packets (Interest and Data) to be transmitted on the link.
  A bare network packet on a NDNLPv2 link SHOULD be interpreted as a NdnlpPacket with no header and trailer, and have the bare network packet as its NdnlpFragment.
This requirement allows a network packet that doesn't need any NDNLP feature to be transmitted without being encapsulated in NDNLPv2 header.
  More importantly, this allows an NDNLPv2 host to accept packets from non-NDNLPv2 hosts.
Interleaving NDNLP and bare packets could be inefficient.

## Slide 22: Header and Trailer
NDNLPv2 features can add fields into NdnlpHeader and NdnlpTrailer.
Every field definition MUST state whether it belongs to the header or the trailer.
Most fields SHOULD be added to the header.
Only fields that cannot be determined before header generation are added to the trailer.
  eg. HMAC signature of header+fragment

## Slide 23: Sequence Number
NdnlpSequence contains a sequence number that is useful to multiple features.
  If no enabled feature is using the sequence number, this field can be omitted.
The sequence number is encoded as fixed length, so that field length is predictable.
  Length of this field is decided on a per-link basis.
A host MUST generate consecutive sequence numbers for outgoing packets on the same face.

## Slide 24: NdnlpNop: padding
NdnlpNop is a padding at the end of NdnlpHeader.
  When a NdnlpHeader parser sees zero in place of TLV-TYPE, it MUST ignore the rest of NdnlpHeader.
This is useful when a NdnlpPacket is directly constructed in an aligned hardware buffer (eg. NIC-mapped memory), but NdnlpHeader size is undecidable before NdnlpFragment is copied into the buffer.

## Slide 25: NdnlpFragment: (fragment of) network layer packet
NdnlpFragment contains a fragment of one or more network layer packets (Interest or Data).
The fragmentation and reassembly feature defines how NdnlpFragment field is constructed and interpreted.
When fragmentation and reassembly feature is disabled, the NdnlpFragment field contains a whole network layer packet.
NdnlpFragment can be omitted. NdnlpPacket without NdnlpFragment is an IDLE packet.

## Slide 26: Field Order
Fields in extensible part of the header and the trailer can appear in any order.

## Slide 27: Unknown Fields
If an incoming NdnlpPacket contains unknown fields, it's dropped.
  However, the host SHOULD NOT consider the link has an error.
Rationale: NdnlpPacket is hop-by-hop. It's feasible to ensure everyone to understand all fields.
Note: if a field is known but the relevant feature is disabled, it's not an "unknown field".
  Field definition SHOULD state what to do when relevant feature is disabled.

## Slide 28: Indexed Fragmentation

## Slide 29: Introduction
Indexed fragmentation provides fragmentation and reassembly feature on datagram links that does not guarantee in-order delivery.
A network layer packet is fragmented into one or more fragments; each fragment can belong to only one network layer packet.

## Slide 30: Operations
Sender slices a network layer packet into one or more fragments, such that the NdnlpPacket carrying every fragment is below link MTU.
Receiver
  stores fragments in PartialMessageStore, indexed by MessageIdentifier = NdnlpSequence - FragIndex
  delivers complete network layer packets to upper layer
  maintains a reassembly timer in each PartialMessage, which is reset each time a new fragment is received; if this timer expires, the PartialMessage is dropped
    default timer duration: 500ms

## Slide 31: Fields
NdnlpSequence is REQUIRED.
Header fields:
  NdnlpFragIndex: 0-based index of this fragment in the network layer packet
  NdnlpFragCount: count of fragments of the network layer packet
If a network layer packet can fit into one fragment, NdnlpFragIndex and NdnlpFragCount MAY be omitted.

## Slide 32: Format Definition
NdnlpFragIndex ::= NDNLP-FRAG-INDEX-TYPE TLV-LENGTH nonNegativeInteger
NdnlpFragCount ::= NDNLP-FRAG-COUNT-TYPE TLV-LENGTH nonNegativeInteger

## Slide 33: Other Header and Trailer Fields
Unless otherwise noted, header and trailer fields of other NDNLPv2 features only appear in the NdnlpPacket that carries the first fragment.

## Slide 34: Example
To transmit a 2000-octet network layer packet on a MTU=1500 link, it's sliced into two fragments:
  Sequence=N+0, FragIndex=0, FragCount=2, (header fields for other features), Fragment=payload[0:1500]
  Sequence=N+1, FragIndex=1, FragCount=2, Fragment=payload[1500:2000]
To transmit a 1000-octet network layer packet on a MTU=1500 link, it's put in one fragment:
  Sequence=N+0, Fragment=payload[0:1000]
  or, Sequence=N+0, FragIndex=0, FragCount=1, Fragment=payload[0:1000]

## Slide 35: B-E Fragmentation

## Slide 36: Introduction
B-E fragmentation provides fragmentation and reassembly feature for a standard layer 2 media that can guarantee in-order delivery.
This design follows the Sequenced-Fragment protocol as defined in draft-mosko-icnrg-hopfragment section 2.

## Slide 37: ARQ Reliability

## Slide 38: Introduction
ARQ reliability improves reliability on a lossy link, using automated repeat requests.
  This reliability improvement is a supplement of strategy retries. It can help improve network performance.
ARQ reliability provides link reliability improvement, not reliability guarantee.

## Slide 39: Basic Operations
Sender caches recent outgoing NdnlpPackets, indexed by sequence number.
  This cache is indexed by sequence number.
  This cache uses FIFO policy, and SHOULD have enough capacity for NdnlpPackets sent in 1.5~2xRTT to be useful.
Receiver detects gaps in sequence numbers. If a missing packet isn't received after 3 later sequence numbers, the receiver transmits a repeat request.
Sender resends NdnlpPackets in reply to repeat requests.

## Slide 40: Example
T (RTTs) | send by | packet | received by | notes
0.0 | A | seq=1, fragment=P | B @0.5 | 
0.1 | A | seq=2, fragment=Q |  | 
0.2 | A | seq=3, fragment=R | B @0.7 | 
0.3 | A | seq=4, fragment=S | B @0.8 | 
0.4 | A | seq=5, fragment=T | B @0.9 | 
0.9 | B | repeat 2 | A @1.4 | 
1.4 | A | seq=2, fragment=Q | B @1.9 | 

## Slide 41: Operations: idle
Sender transmits an IDLE packet, if it hasn't sent anything within last 1xRTT, and the last sent packet is not an IDLE packet.
  This allows receivers to detect a gap in case the last NdnlpPacket is lost.
  But there's no recovery in case the "idle" NdnlpPacket is lost.
If a receiver is missing a packet, it should immediately transmit a repair request without further waiting for 3 later sequence numbers.

## Slide 42: Example: idle
T (RTTs) | send by | packet | received by | notes
0.0 | A | seq=1, fragment=P | B @0.5 | 
0.1 | A | seq=2, fragment=Q |  | 
1.1 | A | seq=3, idle | B @1.6 | 
1.6 | B | repair 2 | A @2.1 | 
2.1 | A | seq=2, fragment=Q | B @2.6 | 

## Slide 43: Operations: multi-access link
On a multi-access link, group-RTT should be used in place of RTT.
On a multi-access link, receivers MAY suppress its own repeat requests to reduce the number of repeat requests for the same sequence number.
  probability based suppression, reference: "DIP: Distance Information Protocol for IDMaps" section 3.3 "feedback suppression"

## Slide 44: Fields
NdnlpSequence is REQUIRED.
  except: NdnlpPacket that carries only NdnlpArq doesn't require NdnlpSequence, unless it's required by another feature.
NdnlpArq header field: contains sequence numbers that need repair.
  SenderAddress is required to indicate the sender on a multi-access link; it's optional on a point-to-point link.
  This can be sent as a standalone NdnlpPacket without NdnlpFragment, or piggy-backed onto another NdnlpPacket that also carries a NdnlpFragment.

## Slide 45: Format Definition
NdnlpArq ::= NDNLP-ARQ-TYPE TLV-LENGTH SenderAddress? NdnlpSequence+
SenderAddress ::= SENDER-ADDRESS-TYPE TLV-LENGTH byte+

## Slide 46: Mostly-Passive Failure Detection

## Slide 47: Introduction
Mostly-passive failure detection provides rapid failure detection of a host on either a point-to-point link or a multi-access group.
A host is considered failed if nothing arrives from that host within Tdead.
  This procedure is passive.
A host transmits an IDLE packet if it hasn't sent anything in last Tidle, in order to convince other hosts that it's alive.
  This is the non-passive, but it won't happen when host is busy.
  Tdead >= 3xTidle

## Slide 48: Operations: full mode
Host periodically transmits IDLE packets,
  if it hasn't transmitted anything in last Tidle.
Full mode is suitable when the host wants to ensure its peer(s) know its aliveness, such as:
  router-router links
  laptop side of laptop-router link

## Slide 49: Operations: passive mode
Host does not periodically transmit IDLE packets.
Host replies an IDLE packet in response to an incoming IDLE packet,
  if it hasn't transmitted anything in last Tidle.
Passive mode consumes less resources (no timer), and is suitable when the host knows its peer(s) is in full mode, such as:
  router side of laptop-router link

## Slide 50: Operations: on multi-access link
A multi-access link can never fail, but a host can detect failures of peers on the link.
As long as at least one host is in full mode, every other host, regardless of its mode, will be transmitting at least one packet every Tidle, either scheduled by timer or as a reply.
  Recall that a passive mode host replies to IDLE packet only if nothing is transmitted in last Tidle, so this won't cause exponential transmissions.

## Slide 51: Caution: WiFi multicast
WiFi multicast is slow, and requires all stations in Low Power mode to stay awake.
It's NOT RECOMMENDED to run this failure detection feature on a multicast group that involves WiFi stations.

## Slide 52: HMAC Integrity

## Slide 53: Introduction
HMAC integrity allows an HMAC signature to be attached to each NdnlpPacket, in order to prevent packet injection.
  This is most useful on a point-to-point datagram tunnel, but can be used on other links as well.
This design assumes the hash algorithm and sender's key are pre-shared,
  eg. during tunnel authentication

## Slide 54: Fields
NdnlpHmacSignature trailer field: HMAC signature covering NdnlpHeader and NdnlpFragment.
  This field is put in the trailer, so that the signature can be generated over a consecutive chunk of octets.
NdnlpTrailer isn't covered by the signature.
  Other fields in the trailer, if any, won't be protected by the signature.
NdnlpHmacSignature field is per-fragment.
  If a network layer packet is fragmented, each fragment gets its own signature.

## Slide 55: Format Definition
NdnlpHmacSignature ::= NDNLP-HMAC-SIGNATURE-TYPE TLV-LENGTH byte+

## Slide 56: Network NACK

## Slide 57: Introduction
A network NACK is a forwarding instruction from upstream to downstream that indicates the upstream is unable to satisfy an Interest.
Network layer packet MUST be an Interest that the upstream is unable to satisfy.
NdnlpNack header field indicates the packet is a NACK instead of a regular Interest.
  It can optionally carry a reason, and a suggestion on what downstream should do.

## Slide 58: Format Definition
NdnlpNack ::= NDNLP-NACK-TYPE TLV-LENGTH Nack?
Nack ::= DuplicateNack | GiveUpNack | NoDataNack | CongestionNack | BusyNack
DuplicateNack ::= DUPLICATE-NACK-TYPE TLV-LENGTH(=0)
GiveUpNack ::= GIVE-UP-NACK-TYPE TLV-LENGTH(=0)
NoDataNack ::= NO-DATA-NACK-TYPE TLV-LENGTH NoForward?
NoForward ::= NO-FORWARD-TYPE TLV-LENGTH Name

## Slide 59: Format Definition
CongestionNack ::= CONGESTION-NACK-TYPE TLV-LENGTH RateSuggestion?
RateSuggestion ::= RATE-SUGGESTION-TYPE TLV-LENGTH Name Rate
Rate ::= RATE-TYPE TLV-LENGTH(=4) IEEE794-binary32-float
BusyNack ::= BUSY-NACK-TYPE TLV-LENGTH RetryAfter?
RetryAfter ::= RETRY-AFTER-TYPE TLV-LENGTH nonNegativeInteger

## Slide 60: Semantics
TODO

## Slide 61: Design Choice: reason types
Why each NACK reason needs a TLV-TYPE instead of a numeric code?
  because additional information and suggestions can be carried in the reason's element.
What's the necessity of outer NdnlpNack element?
  This allows hosts to recognize this is a NACK.
  A host that recognizes NdnlpNack but doesn't recognize the inner reason type SHOULD treat this as a NACK without reason, instead of dropping the packet.

## Slide 62: Design Choice: suggestions
Why are suggestions nested under the reason element, instead of directly under NdnlpNack?
  A suggestion makes sense only under a certain reason.
How is the Name in NoForward chosen?
  A forwarder (not considering policy) never knows which namespace it cannot serve.
  TODO: need an answer

## Slide 63: Consumer Controlled Forwarding

## Slide 64: Introduction
Consumer controlled forwarding allows a local consumer application to explicitly specify the nexthop face to forward an Interest.
Network layer packet MUST be an Interest on which the instruction in NextHopFaceId header field applies.
A host SHOULD follow this instruction and forward the Interest to the specified nexthop.
  ContentStore SHOULD NOT satisfy this Interest, unless NextHopFaceId is a special FaceId that represent the ContentStore.
  FIB nexthops are ignored.

## Slide 65: Format Definition
NextHopFaceId ::= NEXT-HOP-FACE-ID-TYPE TLV-LENGTH nonNegativeInteger

## Slide 66: Local Cache Policy

## Slide 67: Introduction
Local cache policy feature allows a local producer application to instruct ContentStore on whether and how to cache a Data packet.
Network layer packet MUST be a Data packet on which the instruction in CachingPolicy header field applies.
A host MAY follow this instruction.

## Slide 68: Format Definition
CachingPolicy ::= CACHING-POLICY-TYPE TLV-LENGTH NoCache | TimeLimitedCache
NoCache ::= NO-CACHE-TYPE TLV-LENGTH(=0)
TimeLimitedCache ::= TIME-LIMITED-CACHE-TYPE TLV-LENGTH ExpirationPeriod

## Slide 69: Incoming Face Indication

## Slide 70: Introduction
Incoming face indication feature allows the forward to inform local applications about the face on which a packet is received.
IncomingFaceId header field can be applied to Interest or Data packets.

## Slide 71: Format Definition
IncomingFaceId ::= INCOMING-FACE-ID-TYPE TLV-LENGTH nonNegativeInteger