## Slide 1: NFD Forwarding with NACK
Junxiao Shi, 2015-07-29

## Slide 2: Overview
A forwarder sends a NACK to its downstream in response to an Interest when it determines that no Data can be returned.
This document describes necessary changes to support NACK.

## Slide 3: API summary
forwarding pipelines
  void onIncomingNack(Face& face, const Nack& nack) // entered upon incoming NACK
  void onOutgoingNack(const Nack& nack, Face& outFace) // entered when strategy wants to send a NACK
strategy API
  virtual void afterReceiveNack(const Face& inFace, const Nack& nack, shared_ptr<fib::Entry> fibEntry, shared_ptr<pit::Entry> pitEntry)
  void sendNack(shared_ptr<pit::Entry> pitEntry, shared_ptr<Face> outFace, const NackHeader& header);
PIT
  NACKed field on out-record
short-term solution before #2000

## Slide 4: Forwarding Pipelines
(copied from nack_20140731.pptx)
WARNING: does not support multi-access group

## Slide 5: Interest Loop pipeline
Keep this simple for now: unconditionally send NACK-Duplicate when duplicate Nonce is detected.
In the future, strategy could be invoked, because duplicate Nonce may be multi-path arrival instead of loop.
outgoing NACK
reason=Duplicate

## Slide 6: Incoming NACK pipeline
PIT match
receive NACK
trigger strategy: after receive NACK
(drop)
mark out-record as NACKed
N
has out-record?
Y
(drop)
N
Y

## Slide 7: Outgoing NACK pipeline
send NACK
strategy action: send NACK
erase in-record
has in-record?
(drop)
N
Y

## Slide 8: NACKed field in PIT out-record
A NACKed field is added to PIT out-record.
This field is cleared in Outgoing Interest pipeline.
This field is set to the reason code in Incoming NACK pipeline.
The purpose of this field is to help forwarding strategy make decisions.

## Slide 9: Strategies

## Slide 10: Best Route strategy
after receive NACK trigger:
  if any out-record in PIT entry is not yet NACKed, abort these steps
  combine NackReasons remembered in all out-records, pick the least severe NackReason (Congestion < Duplicate < NoRoute)
  send NACK to all downstreams

## Slide 11: Broadcast (or Multicast) strategy
TODO, should be similar to best-route
see #3011

## Slide 12: Access strategy
TODO, should try alternate paths upon NACK

## Slide 13: NCC strategy
NCC is designed to mimic ccnd 0.7.2 which does not support network layer NACK. This strategy will keep unchanged.