## Slide 1: NDNLP Implementation of Best-Effort Link-Layer Reliability
Eric Newberry
The University of Arizona

## Slide 2: Background
Based upon “Hop-By-Hop Best Effort Link Layer Reliability in Named Data Networking” by S. Vusirikala, et al.
Modifications in Redmine issue #3823
  No packet number transmitted, only frame number (Sequence)
  RTO timeout uses traditional TCP RTO equation (SRTT + 4 * RTTVAR)
  After retx reached or packet ACK’d after losses, a notification will be sent to the strategy layer.
The sender sends notifications to strategy layer based upon network-layer packets, not fragmented link-layer packets.
Sequences are required for all packets when BELRP enabled.

## Slide 3: Packet Format
The following headers fields need to be added to NDNLP:
  Ack (64-bit non-negative integer), repeatable

## Slide 4: Sender Subsystem
Store Packet in TransmitCache + set retx[seq] to 0
Assign Sequences
to fragments
Start RTO timeout
Send fragment to Transport
Increment retx[seq], set retransmit flag for NetPkt
Send failure notification to strategy
Search queued ACKs to piggyback
retx[seq] >= maxRetx
No
On Timeout
Remove Packet from TransmitCache
Reset ACK send timeout
Send all pending ACKs in IDLE packets
Fragment NetPkt
For each fragment
Create mapping of all fragments in NetPkt
Yes
On Timeout
Cancel all RTO timeouts for this NetPkt
Delete all fragments of NetPkt from TransmitCache

## Slide 5: Send Process
Insert this subsystem in GenericLinkService after Sequence number assignment.
After fragmenting NetPkt, create a mapping of Sequences to the NetPkt. Also store the number of fragments in the packet, the number of sequences that have been ACK’d or timed out, and a flag indicating whether any fragments had to be retransmitted.
TransmitCache stores all transmitted and to-be-transmitted fragments. Fragments are removed after they are ACK’d or the maximum number of retransmissions (maxRetx) is reached.
After storing the packet in the TransmitCache, start the RTO timeout (SRTT + 4 * RTTVAR -- the method calculating this is discussed later).

## Slide 6: Send Process
Search the ACK queue for any pending ACKs to piggyback. Piggyback as many as will fit on this packet. Reset the ACK send timeout, which allows ACKs to be sent in their own packet if no packet they can piggyback on is transmitted within the timeout.
Finally, the packet is handed to the Transport for transmission.

## Slide 7: Send Process (Timeouts)
On timeout of a fragment, increment retx[seq] and set the flag of the NetPkt indicating whether any fragments needed to be retransmitted to true.
  If retx[seq] is less than the maximum number of retransmissions, restart the RTO timeout for the fragment and continue the transmit process from that point.
  Otherwise, remove the fragment from the TransmitCache, cancel the RTO timeouts for all fragments of this NetPkt, delete all of NetPkt’s fragments from the TransmitCache, and send a failure notification for this NetPkt to the strategy layer (indicating that at least one fragment reached the maximum number retransmissions and was dropped).

## Slide 8: Receiver Subsystem
Extract + Remove Piggybacked ACKs
Cancel fragment’s RTO timeout timer
Remove ACK’d fragments from TransmitCache
Queue ACK to transmit for Packet
Increment number of NetPkt fragments ACK’d/>=maxRtt?
For each received ACK
Reassembly
Receive packet
from Transport
Yes
Are all fragments of NetPkt ACK’d/>=maxRtt?
Send loss notification to strategy
Yes
Is retransmit flag set for NetPkt?

## Slide 9: Receive Process
Insert this subsystem in GenericLinkService before fragment reassembly.
If the LpPacket does not have any ACKs piggybacked, immediately send it to reassembly and skip this process.
Extract and remove piggybacked ACKs from the LpPacket. For each ACK, do the following:
  Check that an RTO timeout is running for this Sequence. If not, ignore the ACK.
  Cancel the fragment’s RTO timeout and remove the fragment from the TransmitCache.
  Increment the number of fragments for this NetPkt that have been ACK’d or have reached the maximum number of retransmissons.
  If all fragments of the NetPkt have been ACK’d or have reached the maximum number of retransmissions, and the flag indicating whether any fragments for this packet needed to be transmitted is set to true, send a loss notification for this NetPkt to the strategy layer (indicating that all fragments were received, but some needed to be retransmitted).

## Slide 10: RTO Calculation
RTO is calculated using the standard TCP RTO formula (SRTT + 4 * RTTVAR).
RTT is measured as the difference between the time the fragment was transmitted and the time an ACK was received for it.
Fragments with one or more retransmissions are not taken into account when calculating the RTO.